## Slide 1
Approximate ECC via Feistel-Permuted CRC Hashing
Burst resilience, overhead scaling, and failure mode characterization
Research Presentation · 2026
Notes: Lead with burst immunity — that is the primary justification.

## Slide 2
Why BCH Fails on Burst Errors
BCH is designed for the BSC (random error model) — burst channels violate this assumption
How BCH is deployed in practice
▸ Applied to small blocks: typically 256 bits per codeword
▸ t = expected errors per block = round(BER × 256)
▸ e.g. t=13 at 5% BER → 45.7% overhead per block
▸ Tiled across larger data: 16 × BCH(256) for 4096-bit page
▸ Each block independently decodes — no cross-block awareness
▸ Assumes random, independent errors per block (BSC model)
The burst problem
▸ Flash, DRAM, fiber produce burst errors — not random flips
▸ A burst of b bits may land entirely in one 256-bit block
▸ If b > t: that block fails completely — even if all other blocks are clean
▸ At 5% BER with t=13: any burst > 13 bits in one block = failure
▸ 13 bits is a tiny burst — real channels produce bursts of 100s of bits
▸ BCH has no mechanism to handle this: it was designed for random channels
Notes: Sets up the empirical proof on the next slide.

## Slide 3
BCH Burst Failure vs Our Scheme — Empirical
BCH (16×256-bit blocks, t=13, 45.7% OH) vs CRC-32 (100% OH) · 5% BER operating point · 30 trials
What the data shows
BCH (red):
▸ 100% success for burst ≤ 13 bits
▸ Hard cliff at burst = 14+ bits
▸ 45.7% overhead buys only 13-bit burst tolerance
Our scheme (blue):
▸ 100% success through burst = 245 bits
▸ No cliff anywhere in tested range
▸ Feistel permutation scatters any burst uniformly — solver sees random errors regardless
BCH fails at 14 bits. Ours handles 245 bits.
Notes: Say nothing. Let the cliff speak.

## Slide 4
Overhead: BCH vs Our Scheme
t = round(BER × 256) · 16 × BCH(256-bit blocks) vs CRC-32 on 4096-bit data
BER | BCH t (expected errors) | BCH overhead | Our CRC-32 | BCH burst tolerance
1% | t=3 | 10.5% | 100% | 3 bits
2% | t=5 | 17.6% | 100% | 5 bits
3% | t=8 | 28.1% | 100% | 8 bits
4% | t=10 | 35.2% | 100% | 10 bits
5% | t=13 | 45.7% | 100% | 13 bits
6% | t=15 | 52.7% | 100% | 15 bits
Our burst tolerance: 200+ bits at every BER ✓
BCH wins on overhead — but only works for random errors.
Why we are still positioned better
▸ BCH t is the expected error count — but channels produce bursts, not uniform random errors
▸ A 14-bit burst at 5% BER lands in ONE 256-bit block and immediately exceeds t=13 → hard failure
▸ BCH requires adding an interleaving layer for burst protection — extra complexity and latency
▸ Our Feistel permutation handles bursts natively: scatters any burst across 4096 bits, solver always sees ~uniform distribution
▸ Decode cost: CRC checks are 10–30× cheaper than BCH Galois Field operations
▸ No per-block failure mode: a burst that crosses block boundaries in BCH can fail multiple blocks simultaneously
Notes: BCH wins on overhead — state this directly. Then pivot to burst tolerance column.

## Slide 5
What Our Scheme Corrects — 4096-bit block, 30 keys
CRC-8 / CRC-16 / CRC-32 — success rate, solve time, and hash comparisons vs flip count
CRC-32 (100% OH)
100% success through 266 flips (~6.5% BER) — full tested range
CRC-16 (50% OH)
100% through 100 flips; graceful degradation
CRC-8 (25% OH)
Cliff at 40 flips. Fast 'solve' is SDC not speed
Notes: CRC-32 is the safe operating mode. CRC-8 fast solve time is SDC — explained on the safety slide.

## Slide 6
Our Scheme: Burst = Random — CRC-32, 4096-bit, 30 keys
Feistel permutation makes burst errors indistinguishable from random errors for the solver
Key results
▸ Random and burst success curves overlap perfectly at all flip counts
▸ Solver search effort also nearly identical
▸ At 200 flips (~4.9% BER): 100% for both random AND burst
▸ BCH would fail on burst > 13 bits here (slide 3)
▸ Burst immunity is free — a byproduct of the permutation, not an add-on
Notes: This is the payoff for slide 2. Curves overlapping is the entire result.

## Slide 7
When Does the Solver Succeed? — The Flips-per-Node Model
A single variable predicts success across all block sizes, hash widths, and BER values
Flips per row-node = flip count ÷ √L (√L = number of row-groups in the grid = average solver load per DAG node)
Hash | Safe (≥95%) | Degrading | Failed (~0%)
CRC-16 | < 1.6 | ~2.2 | > 3.2
CRC-32 | < ~4.0 | ~4.0–4.5 | > 4.5 (not yet characterised)
CRC-32 tolerates higher flips/node due to a stronger hash (1/4B false-positive rate vs 1/65K for CRC-16).
Evidence across experiments:
Hash | L | Flips | Flips/node | Success
CRC-32 | 1024 | 51 | 1.59 | 100%
CRC-32 | 4096 | 266 | 4.16 | 100%
CRC-16 | 1024 | 51 | 1.59 | 100%
CRC-16 | 2048 | 102 | 2.22 | 70%
CRC-16 | 4096 | 204 | 3.19 | 0%
CRC-32 | 4096 | 204 | 3.19 | 100%
Why this variable?
▸ √L = number of row-groups → flips ÷ √L = average load per solver node
▸ Collapses Fig 1, Fig 2, Fig 3, and Fig 6 onto a single predictive axis
▸ Design rule: keep flips/node < 1.6 for reliable operation
▸ Threshold values are empirical — out-of-sample validation (L=768, 3072) is proposed next
Notes: This is the theoretical contribution. Functional form is from the architecture; thresholds are empirical.

## Slide 8
Safety: Silent Data Corruption
When does the solver return wrong bits without detecting failure? 50 keys/cell
Config | SDC rate | Status
CRC-8, gs=1 | 78.6% | ⚠ Unsafe
CRC-16, gs=1 | 14.2% | ⚠ Risky
CRC-16, gs=2 | ~0% | ✓ Safe
CRC-32, gs=1 | 0% | ✓ Safe
CRC-32: zero silent errors across all tested configurations.
▸ SDC: solver returns a wrong bitstring that satisfies all hash checks
▸ CRC-8 'solves fast' because it accepts false positives — it's not efficient, it's wrong
▸ CRC-32 false-positive rate: 1 in 4 billion — zero SDC observed
▸ CRC width selection is a safety boundary, not a performance knob
Notes: Present CRC-8 number without softening. You found it — that's intellectual credit.

## Slide 9
Summary
 | Our scheme (CRC-32) | BCH (256-bit blocks)
Overhead at 5% BER | 100% | 45.7% ← BCH wins
Burst tolerance | 200+ bits ✓ | 13 bits ✗
Correction guarantee | Probabilistic | Deterministic ✓
SDC risk | 0% ✓ | 0% ✓
Decode cost | CRC checks ✓ | GF field ops
Overhead scaling | O(1/√L) ✓ | Flat
Key results:
▸ BCH fails on bursts > t bits — demonstrated empirically (slide 3)
▸ Our Feistel permutation converts bursts to uniform errors — burst and random curves overlap
▸ CRC-32: 100% success through 6.5% BER, zero SDC
▸ Flips/node < 1.6 is the design rule for reliable operation
▸ BCH wins on overhead for random errors — our advantage is burst channels
The case for this scheme:
For any channel where errors cluster (flash retention, DRAM row-hammer, fiber interference), BCH's small per-block t budget is exceeded by real bursts. Our Feistel permutation neutralises this structurally — no interleaving layer required, no burst-length assumption, at a decode cost 10–30× lower than BCH. The overhead premium (~2× at 5% BER) is the price of that robustness.
Notes: This is the closing argument. Read the bottom paragraph aloud.